## Slide 1: CANBus Reversing

## Slide 2: CANBus Reversing
IDs
  Unique
  Frequency
Data
  anomalous
  graphing/trending
PID Standards
  SAE J/1979
  Majority of PIDs are non-standard

## Slide 3: PID Standards
SAE J/1979 dictates some
Most are non-standard proprietary with little overlap
Database at ETI for the low low price of $7500

## Slide 4: We need some tools
Unique ID finder
ID frequency
Data trends

## Slide 5: CANBus IDs and Messages
Bus is saturated by messages
Components use ID to communicate
Each Make & Model may vary
Requires Reverse engineering to identify

## Slide 6: RPM example
Toyota:
RPM is sent over ID 0x2C4 as a big endian 16 bit integer at offset 0 (the messages are always 8 bytes)

## Slide 7: RPM Example
See readrpm.js to display RPMs
canreplay -I diags/ingition.log vcan0=can0

## Slide 8: Reversing IDs
Reverse engineering the protocols used by manufacturers can be difficult and there is no standard (hence OBDII PIDs)
Requiring bus write to get engine data is inherently insecure

## Slide 9: Reversing IDs
Search the internet for projects such as http://tucrrc.utulsa.edu/ToyotaCAN.html