## Slide 1
Programming in Python
For CAN
K. Reid Wightman
Director, Digital Bond Labs

## Slide 2: Python
Fun scripting language, widely-used by hackers
Log in to your Beagle Bone and run
root@beaglebone:~# python
Python 2.7.3 (default, Mar 14 2014, 17:55:54)
[GCC 4.6.3] on linux2
Type "help", "copyright", "credits" or "license" for more information.
>>>

## Slide 3: Python CAN Basics
Python 2.7.3 (default, Mar 14 2014, 17:55:54)
[GCC 4.6.3] on linux2
Type "help", "copyright", "credits" or "license" for more information.
>>> import can
>>> help(can) # shows help on can module
>>> mybus = can.interfaces.socketcan_ctypes.Bus(“can0”)
>>> message = mybus.recv() # this will hang

## Slide 4: Python CAN Basics
Log on to another shell and type
# ip link add vcan0 type vcan
# ifconfig vcan0 up
# cansend vcan0 1f4#41414141

## Slide 5: Python CAN Basics
Python 2.7.3 (default, Mar 14 2014, 17:55:54)
[GCC 4.6.3] on linux2
Type "help", "copyright", "credits" or "license" for more information.
>>> import can
>>> help(can) # shows help on can module
>>> mybus = can.interfaces.socketcan_ctypes.Bus(“can0”)
>>> message = mybus.recv() # now this finishes
>>> message.arbitration_id # message priority
500L
>>> message.data # data payload
bytearray(b'AAAA’)

## Slide 6: Python CAN Basics
Send a message:
>>> responsemessage = can.message.Message(arbitration_id = 500, data = "")
>>> myBus.send(responseMessage)
Note: can.message.Message() defaults to using extended arbitration ids!
>>> responsemessage = can.message.Message(extended_id = False, arbitration_id = 500, data = "")

## Slide 7: Challenge 1
SSH to your beaglebone
Look in Challenge1-2 directory
  # cd Challenge1-2
Run the ‘canping’ utility
  # ./canping <interface>
This application puts PING packets on the CAN interface

## Slide 8: Challenge 1
HOWTO
Use Python to listen for a packet (myBus.recv())
Generate an acknowledgement packet
  For round 1, it doesn’t need to have any data
  See example a few slides back
Wrap the while thing in a ‘while’ loop
In Python:
while True:
myBus.recv() # listen for data
# now build a response message
# now send the response

## Slide 9: Python: Working with Data
You should now have the password for challenge 2
Challenge 2 is a lot harder =)
In this challenge, you need to parse data from the CAN packet, for use in the response
Here are some tips for building packets…

## Slide 10: Python: Manipulating Data
Run ‘canping’ utility with mode 2
Capture a packet in Python
Now, let’s look at the data part
>>> message.data
bytearray(b'8\x00xPING')’)
The \x part tells us this is not ASCII data
This is actually 0x38, 0x00, 78, 0x50, 0x49, 0x4E, 0x47

## Slide 11: So what do the bytes mean?
Watch the values for a while, notice a pattern?

## Slide 12: So what do the bytes mean?
Watch the values for a while, notice a pattern?
First byte is random

## Slide 13: So what do the bytes mean?
Watch the values for a while, notice a pattern?
First byte is random
Second byte is always 0x00

## Slide 14: So what do the bytes mean?
Watch the values for a while, notice a pattern?
First byte is random
Second byte is always 0x00
Third byte is incrementing

## Slide 15: So what do the bytes mean?
Watch the values for a while, notice a pattern?
First byte is random
Second byte is always 0x00
Third byte is incrementing
Then it’s always ASCII ‘PING’

## Slide 16: The Goal
Reply to the PING messages by sending a PONG response
The first two bytes are the ‘source address’ of the PING, so you need to address the response using that as the arbitration id
The next byte is a sequence identifier, you need to use the same sequence identifier
The response to a PING should be ‘PONG’
Want a candump of successfully satisfying the challenge?

## Slide 17: Some Python to help
>>> mystring = str(message)
‘8\x00xPING’
>>> mystring[0]
‘8’
>>> ord(mystring[0])
56
>>> newArbId = ord(mystring[0])

## Slide 18: Solve the problem the easy way first
Grab the bytes you need from message.data
Rebuild response packets
Loop it

## Slide 19: Solve the problem the prettier way later
Using Python ctypes and a data structure…
Kind of like rocket science
  except it doesn’t involve rockets
  and it isn’t hard

## Slide 20: Python ctypes
Problem: parsing message.data is ugly
Many protocols impose a data structure on it
Let’s apply a data structure to it
PingPongMessage {
source address; // 2 byte address
sequence id; // 1 byte id
command; // string
}

## Slide 21: Python ctypes
from ctypes import *
class PingPongMessage(Structure):
_fields_ = [("destaddr", c_ushort),
("seqid", c_byte),
("command", c_char*5) ]

## Slide 22: Python ctypes
Make a PingPongMessage
ppMsg = PingPongMessage()
incomingmessage = myBus.recv()
incomingdata = incomingmessage.data
fit = min(len(incomingdata), ctypes.sizeof(ppMsg))
ctypes.memmove(ctypes.addressof(ppMsg), str(incomingdata), fit)
Now ‘ppMsg’ contains the CAN data payload, but with PingPongMessage structure applied
You can pull out the portions using ppMsg.destaddr, ppMsg.seqid, ppMsg.command

## Slide 23: Python CAN Basics
Ping-Pong example
Start running the ‘ping’ application
  It sends CAN frames, expecting a response
  We need a ‘pong’ application that will send the responses that ‘ping’ expects
  If you can satisfy the ‘ping’ application for a while, it will unlock another surprise
Multiple ways to solve the problem.
  Bonus points if you use CyclicSendTask
Have Fun!