## Slide 1: CANBus Analysis

## Slide 2: Tools
Beaglebone Black
Serial Cape
SocketCAN
can-utils
Language of your choice (...kind of)

## Slide 3: BeagleBone Black

## Slide 4: Serial Cape
Beaglebone device tree allows for runtime loading of hardware
Pre-installed debian comes with .dtb for the serial cape you have

## Slide 5: SocketCAN
CANbus stack for the Linux kernel (thank you Volkswagon Research)
Sets up CAN as a network device
This means you can use much linux for many profits, CAN is just sockets

## Slide 6: SocketCAN
#define CAN_EFF_FLAG 0x80000000U /* EFF/SFF is set in the MSB */
#define CAN_RTR_FLAG 0x40000000U /* remote transmission request */
#define CAN_ERR_FLAG 0x20000000U /* error message frame */
typedef __u32 canid_t;
#define CAN_MAX_DLC 9
#define CAN_MAX_DLEN 8
struct can_frame {
canid_t can_id; /* 32 bit CAN_ID + EFF/RTR/ERR flags */
__u8 can_dlc; /* frame payload length in byte (0 .. CAN_MAX_DLEN) */
__u8 data[CAN_MAX_DLEN] __attribute__aligned(8);
};

## Slide 7: Device Configuration
# ip link set can0 type can help
# ip link set can0 up type can bitrate 500000

## Slide 8: can-utils

## Slide 9: vcan
# modprobe vcan
# ip link add vcan0 type vcan
# ip link set vcan0 up

## Slide 10: candump
Useful program for dumping canbus messages for offline analysis

## Slide 11: candump
# candump -cae any,0:0,#FFFFFFFF
# candump -l can0,0:0#FFFFFFFF

## Slide 12: cansend
used to send messages over canbus

## Slide 13: cansend example

## Slide 14: canplayer
Canplayer is a utility to replay the output of a candump onto a device
We will be using this to replay messages on a virtual CAN device

## Slide 15: canplayer
$ canplayer vcan0=can0 < /path/to/candump/log
If you have candump listening on vcan0, you should see some frames

## Slide 16: Language of your choice

## Slide 17: OBDII PIDs
Bus will be filled with standard sensor data
Diagnostics tools have a query-response mechanism for getting information from an ECU

## Slide 18: Standard OBD PID
Diagnostic reader initiates on ID 0x7DF
Each ECU on the bus (usually 1) will respond with their “ID” + 8. ECU “IDs” start at 0x7E0 and go to 0x7E8
Thus ECU will respond on PID 0x7E8

## Slide 19: Standard OBD Response
Vehicle responds to PID with ID depending on the module responding.
Typical Engine ECU is 0x7E8
Prius hybrid and battery controllers are 0x7E9,0x7EA,etc